## Slide 2
Effects Of Controls – 3 Axis

## Slide 3
AIM
To operate the primary and ancillary controls in flight and on the ground and feel and understand the primary, secondary, and further effects they have on the aircraft.

## Slide 4
APPLICATION
Visual flight focus outside cockpit
Control grip & feel
Cockpit layout/adjustments
Demonstrate/practice sequence
Introduction of pre/post flight actions

## Slide 5
UNDERPINNING THEORY

## Slide 6
Lift
As air flows over the wing, increased speed above the wing results in reduced pressure = Lift
Lift can be altered by changing the shape of the wing, the angle of attack, and the airspeed

## Slide 7
Primary Controls
Elevator pitches aeroplane – changing attitude
Aileron rolls aeroplane – changing direction
Rudder yaws aeroplane – balanced flight
Slipstream affects the rudder and elevator

## Slide 8
Ancillary Controls
Trim tabs provide a force to hold primary controls
Flap changes shape of wing, increases lift, drag, and L/D ratio – changes pitch-trim change required
Carburettor heat assists in preventing and reducing icing in the fuel delivery system

## Slide 9
FLIGHT EXERCISE

## Slide 10
ON THE GROUND
Control speed with throttle and brakes
One hand on control column and other on throttle
Dual controls fitted
Power – controls movement
Brakes – control slowing/stop
Pedals – control steering

## Slide 11
Axis | Control | Input |  | Primary Effect |  | Secondary/Further | Use
Lateral | Elevator | Control Column | forward rearward | Pitch | down up | - | Attitude and Airspeed
Longitudinal | Aileron | Control Column | right left | Roll | right left | Slip - Yaw | Direction
Normal | Rudder | Rudder Pedals | left right | Yaw | left right | Skid - Roll | Balance
IN THE AIR
Attitude flying is achieved by referencing nose and wings to the horizon

## Slide 12
Increased airspeed – firmer control feel & response rate, less movement needed
Decreased airspeed – reduced control feel & response rate, more movement needed
Increased power  increased slipstream
Airspeed
Slipstream
Increased flow over elevator  more effective control
Affects vertical surfaces  yaw
Effect balanced with rudder

## Slide 13
Power decrease  nose pitches down/yaws right
Power increase  nose pitches up/yaws left
Must balance with rudder
Power
Trim
To relieve the pressure
If holding back pressure – trim backwards
If holding forward pressure – trim forwards

## Slide 14
Extending flap  increase in lift and drag  pitch change – trim change required
Retracting flap  decrease in lift and drag  pitch change – aircraft will sink
Flap

## Slide 15
✓
✓
✓
✓
VFR – see and be seen
Clock code, relative height/distance
Horizon is main reference
Control handover process – CRM “I have control/you have control”, “follow me through”
AIRMANSHIP AND HUMAN FACTORS
✓
✓
✓
Land features
Limitations on lookout – S.A.
Limitations of memory
✓
✓
✓
✓
More comfortable with practice/workload
Uncoordinated lesson by nature
Demonstration/practice process - CRM
Self assessment – I.M.S.A.F.E

## Slide 16
OUTCOMES & EXPECTATIONS
Student identifies and understands control and responses
Can identify and reference the horizon correctly
Is comfortable in the airborne environment

## Slide 17
QUESTIONS?

## Slide 18
www.raa.asn.au