## Slide 2
Stalling – 3 Axis

## Slide 3
AIM
To identify the situations where the aircraft is likely to stall and recognise pre-stall symptoms. When stalled adopt the appropriate recovery actions for minimum height loss.

## Slide 4
APPLICATION
Any phase of flight where critical A of A is exceeded

## Slide 5
UNDERPINNING THEORY

## Slide 6
Breaks away from upper surface, aircraft sinks, nose pitches down
Smooth airflow over the wing breaks down and becomes turbulent
L = Angle of Attack x Airspeed

## Slide 7
At the stall
When the wing stalls there is a ↓ in L and a large ↑ in D
Aircraft sinks, C of P moves rearwards  pitch down
Stalls result from exceeding critical Angle of Attack
The elevator controls the A of A of wing
Lift/Drag curve
Airspeeds are referenced in POH in relation to stalling
Stall Speed increase in turning flight due to increased “loading”

## Slide 8
FLIGHT EXERCISE

## Slide 9
HASELL check (Minimum height I.A.W. RAAus Operations Manual)
Adopt slow flight to identify symptoms and reduced control
Entry
Recognition of the stall point in various configurations
Practice and develop recovery actions for min height loss in stall including any ‘incipient’ rotation
Demonstration and understanding of developing conditions due to mishandling of controls or lack of recognition
Carb heat HOT
Practice and recognition of pre-stall scenarios and appropriate actions
Close throttle
Keep straight with rudder
Maintain altitude with backpressure

## Slide 10
Low and decreasing airspeed
Symptoms
Possible high nose altitude
Less effective controls – higher stick forces
Stall warning – if fitted
Control column will be fully back – no further control movement, past stall stick position
Buffet (turbulent air from wing striking tailplane)
High sink rate often undetected

## Slide 11
At the stall
Aircraft sinks and nose pitches down
If aircraft yaws/rolls correct with opposite rudder only - do not use ailerons

## Slide 12
Unstall Wing
Check forward with control column to reduce angle of attack
Do not use ailerons, maintain heading with rudder only
Aeroplane will descend
Recover to S+L with PAT
Recovery
To Minimise Height Loss – max of 100 ft
Power + Attitude + Performance
Unstall, as above, check forward
Apply full power – balance with rudder
Raise nose to the horizon to reduce sink
Lowering attitude assists acceleration
Regain height and S+L

## Slide 13
Recovery at Onset
Normal situation
Recover at stall warning/buffet
Height loss – 50 ft maximum

## Slide 14
✓
✓
✓
✓
Counterintuitive responses and fear TEM
Mismanagement and distraction SA
Recognition of loss of primary control functions
Lookout - Situational Awareness SA
AIRMANSHIP AND HUMAN FACTORS
✓
✓
Limitations in identifying sink rate (Vestibular)
Adherence to personal minimums and airspeed management

## Slide 15
OUTCOMES & EXPECTATIONS
Define the stalled condition
Developed recognition of all pre-stall symptoms in flight
Pilot can state likely scenarios where stalling may occur
Apply timely and appropriate corrective actions
Required recovery standard: Height loss <200 ft, Heading maintenance +/- 10 degrees, Airspeed within Va/Vfe

## Slide 16
QUESTIONS?

## Slide 17
www.raa.asn.au